## Slide 1
Propane: Programming
Distributed Control Planes
Ryan Beckett (Princeton, MSR)
Ratul Mahajan (MSR)
Todd Millstein (UCLA)
Jitu Padhye (MSR)
David Walker (Princeton)

## Slide 2: Configuring Networks is Error-Prone
50-80% of outages are the result of human error
-Juniper 2008
~60% of network downtime is caused by human error
-Yankee group 2002

## Slide 3: Configuring Networks is Error-Prone
“Close to 3 in 4 of all new prefix advertisements were results of misconfiguration”
~1500 ASes affected by outages every day

## Slide 4: Configuring Networks is Error-Prone

## Slide 5: Objectives Mechanisms
Objectives: Network-wide
  Prefer traffic go through AT&T over Sprint
  Don’t use our network as transit between A and B
  Traffic must stay within national boundaries
  Adhere to policies even when failures occur
GAP

## Slide 6: Objectives Mechanisms
Objectives: Network-wide
  Prefer traffic go through AT&T over Sprint
  Don’t use our network as transit between A and B
  Traffic must stay within national boundaries
  Adhere to policies even when failures occur
GAP

## Slide 7: Objectives Mechanisms
Objectives: Network-wide
  Prefer traffic go through AT&T over Sprint
  Don’t use our network as transit between A and B
  Traffic must stay within national boundaries
  Adhere to policies even when failures occur
Mechanisms: Device-by-Device
  Local decisions made independently on each device
  Several device-level actions together imply some higher-level behavior
  Failures interact with local decision-making algorithms in complex ways
GAP
“a large backbone network may have a thousand different policies
configured across hundreds of routers” [Feamster 2005]

## Slide 8: Why use BGP?
BGP in the Wild
  Inter-domain routing between Autonomous Systems (AT&T, Sprint)
  Intra-domain routing in data centers
Advantages
  Allows for local policy among nodes
  Massively scalable — hundreds of thousands of IP prefixes
  Fully distributed — does not require global knowledge of network state
AT&T
Sprint
Notes: If so hard to configure, why is BGP used, and how is it used?

## Slide 9: What about SDN?
Software Defined Networks
  Simpler, centralized programming models
  Network-wide abstractions like paths
  Centralized controller programs the network
But they are not a panacea:
  Do not usually help with inter-domain routing
  Latency, and scalability can be problematic for large networks
  Require careful design and engineering to be robust to failures
  Their implementations don’t exploit existing network infrastructure

## Slide 10: Propane: Programming a Distributed Control Plane
I) Language for expressing high-level operator objectives with:
  Network-wide programming abstraction
  Uniform abstractions for intra- and inter-domain routing
  Paths constraints and relative preferences with fall-backs in case of failures
AS 1
AS 2
AS 3

## Slide 11: Propane: Programming a Distributed Control Plane
2) Compiler to generate a low-level distributed implementation:
  Efficient algorithms to synthesize a set of policy-compliant BGP configs
  Static analysis guarantees policy compliance under all failures
￼
Backup
Network partition — drop

## Slide 12: Border Gateway Protocol (BGP)
  Routers send advertisements for a destination (e.g., 16.4.0.0/16)
  Advertisements contain the AS path traffic would take
  Each router applies local policy to choose best route
    Import filters drop advertisements or modify attributes
    Highest preference is chosen. Path length as a tie breaker
    Export filters drop advertisements or modify attributes
X
local-pref←100
local-pref←99
tag(“foo”)

## Slide 13: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A

## Slide 14: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
path = A
path = A
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A

## Slide 15: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A

## Slide 16: Border Gateway Protocol (BGP)
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
path = CA
X
X

## Slide 17: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A

## Slide 18: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
path = BCA
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A
X

## Slide 19: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A

## Slide 20: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A
path = BA

## Slide 21: Border Gateway Protocol (BGP)
A
C
B
E
D
16.4.0.0/16
advertisement
pkt forwarding
1. Prefer B over A
2. Tag routes “red”
3. Don’t export to E
1. Block “red” routes
1. Prefer C over A

## Slide 22: Border Gateway Protocol (BGP)
A
D
C
E
16.4.0.0/24
16.4.1.0/24
B
16.4.2.0/24
16.4.0.0/16
Aggregation (Route summarization)
  Advertise a more general subnetwork
  Information hiding for routers
  Reduces router table size and improves stability

## Slide 23: Example 1: Backbone Network
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2

## Slide 24: Example 1: Backbone Network
tag(“Peer”)
16.4.0.0/16
block(“Peer”)
Goals
  Prevent transit between peers ($$$)
tag(“Peer”)
block(“Peer”)
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2

## Slide 25: Example 1: Backbone Network
tag(“Peer”)
16.4.0.0/16
block(“Peer”)
Goals
  Prevent transit between peers ($$$)
  Prefer R2 > R1 > Peer ($$$)
tag(“Peer”)
block(“Peer”)
lp←100
lp←99
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2
lp←101

## Slide 26: Example 1: Backbone Network
tag(“Peer”)
16.4.0.0/16
block(“Peer”)
Goals
  Prevent transit between peers ($$$)
  Prefer R2 > R1 > Peer ($$$)
  Filter customer by prefix (security)
tag(“Peer”)
block(“Peer”)
lp←99
filter(16.4.0.0/16, _Princeton)
lp←100
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2
lp←101
filter(16.4.0.0/16, _Princeton)

## Slide 27: Example 1: Backbone Network
define Peer = {Sprint, Level3}
define transit(X,Y) = enter(X) and exit(Y)
define NoTransit = {
true => !transit(Peer,Peer)
}
  Prevent transit between peers
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2

## Slide 28: Example 1: Backbone Network
…
define Preferences = {
true => exit(R2 >> R1 >> Peer)
}
  Prefer R2 > R1 > Peer
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2

## Slide 29: Example 1: Backbone Network
…
define Ownership = {
16.4.0.0/16 => end(Princeton),
}
define Main =
Preferences & Ownership & NoTransit
16.4.0.0/16
Sprint
Level3
Princeton
Cust
R1
R2
  Filter customer by prefix

## Slide 30: Example 2: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers

## Slide 31: Example 2: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
Attempt (1)
  X and Y allow adv. from C,D to peers
  X and Y do not allow adv. from G,H to peers
  Aggregate to PG externally
PG
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers

## Slide 32: Example 2: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
PG
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers
Attempt (1)
  X and Y allow adv. from C,D to peers
  X and Y do not allow adv. from G,H to peers
  Aggregate to PG externally

## Slide 33: Example 2: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers
Attempt (1)
  X and Y allow adv. from C,D to peers
  X and Y do not allow adv. from G,H to peers
  X and Y drop routes through each other
  Aggregate to PG externally

## Slide 34: Example 2: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers
Attempt (1)
  X and Y allow adv. from C,D to peers
  X and Y do not allow adv. from G,H to peers
  X and Y drop routes through each other
  Aggregate to PG externally
PG
PG

## Slide 35: Example 2: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
Goals
  Local prefixes reachable only internally
  Global prefixes reachable externally
  Aggregate global prefixes as PG
  Prefer leaving through Peer1 over Peer2
  Prevent transit traffic between peers
Attempt (1)
  X and Y allow adv. from C,D to peers
  X and Y do not allow adv. from G,H to peers
  X and Y drop routes through each other
  Aggregate to PG externally
Traffic
for PG1
dropped
Aggregation Black hole!

## Slide 36: Example 2: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
define PL1 = 1.0.0.0/24
…
define Ownership = {
PG1 => end(A),
PG2 => end(B),
PL1 => end(E),
PL2 => end(F),
true => exit(Peer1) >> exit(Peer2)
}
Basic reachability for prefixes

## Slide 37: Example 2: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
…
define Locality = {
PL1 or PL2 => always(in)
}
Local services stay internal

## Slide 38: Example 2: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
…
define Locality = {
PL1 or PL2 => always(in)
}
define NoTransit = {
true => ! transit(Peer,Peer)
}
Prevent transit traffic

## Slide 39: Example 2: A Data Center Network
Global
Services
Local
Services
PG1
PG2
PL1
PL2
Peer2
Y
X
D
C
A
B
E
F
H
G
Peer1
Y
C
D
A
B
G
H
E
F
…
define Main =
  Ownership & Locality & NoTransit
  & agg(PG, in → out)
Prevent transit traffic

## Slide 40: Propane Compiler

## Slide 41: Propane Compiler

## Slide 42: Propane Compiler

## Slide 43: Propane Compiler

## Slide 44: Propane: Summary
High-level language
  Single, network-wide policy
  Program using constraints and preferences
  Create new, reusable abstractions (e.g., transit traffic)
  Configure the network modularly
Compiler
  Automatically generates filters, preferences, community values, etc
  Static analysis guarantees policy compliance under all failures
  Lower bound on failures for aggregation-induced black holes

## Slide 45: Compilation
Propane
Regular
IR
Product
Graph IR
…
Quagga
Front End Constraint Language
Regular Expression-based IR
Failure
Analyses
Vendor-independent BGP
Vendor-specific configurations
Abstract
BGP
Topology

## Slide 46: Propane Regular IR (RIR) Syntax
p ::= c1, …, cn
c ::= t1 ↦ r1 >> … >> rn
t ::= true
| (t1 | t2)
| t1 & t2
| prefix=x
r ::= n
| ∅
| in
| out
| (r1 | r2)
| r1 & r2
| r1 · r2
| !r
| r*
Regular expression
path constraints
Traffic predicates
Path Preferences

## Slide 47: Propane Examples:
  in*.(X >> Y).D
Go through either X or Y, but prefer to go through X if possible to get to D
Use path ABC if possible (e.g., failures), otherwise use XYZ
  A.B.C >> X.Y.Z
Use locations A,B,C,D but always prefer A,B to C,D at each hop if possible
  ((A|B) >> (C|D))*
Disallow any transit traffic (i.e., traffic that goes through our network)
  !(out+.in*.out+)

## Slide 48: Propane Regular IR
Propane
Regular
IR
define Ownership =
{PG1 => end(A)
PG2 => end(B)
PL1 => end(E)
PL2 => end(F)
true => exit(Peer1 >> Peer2)}
define NoTransit =
{true => !transit(Peer,Peer)}
define Locality =
{PL1 | PL2 => always(in)}
define Main =
Ownership & Locality & NoTransit
      & agg(PG, in -> out)
Step 1: Combine modular constraints

## Slide 49: Propane Regular IR
Propane
Regular
IR
PG1 => !transit(Peer,Peer) & end(A)
PG2 => !transit(Peer,Peer) & end(B)
PL1 => !transit(Peer,Peer) & always(in) & end(E)
PL2 => !transit(Peer,Peer) & always(in) & end(F)
true => !transit(Peer,Peer) & exit(Peer1 >> Peer2)
Prefix-by-prefix intersection of constraints

## Slide 50: Propane Regular IR
Step 2: Expand constraints in to regular expressions
  exit(X) =
  (out*.in+.(X ∩ out).out*)
  (out*.in*.(X ∩ in).out+)|
  any = out*.in+.out*
  end(X) = (Σ*.X)
Propane
Regular
IR
Step 3: Reduced syntax
  always(X) =
  (X)*
  true => A.(X >> Y).out*
  true => (A.X.out*) >> (A.Y.out*)
  start(X) =
  avoid(X) =
  waypoint(X) =
  (X.Σ*)
  (!X)*
  (Σ*.X.Σ*)

## Slide 51: Propane Regular IR
Problem Formulation
  Policy of the form:
  Semantics — sets of ranked topology paths (preference, length)
  t ↦ r1 >> … >> rn
  rank(p) = (mini p∈ℒ(ri), |p|)
  Determine device-by-device filters, tags, local-preferences so a most preferred path is always obtained.
AS 1
AS 2
AS 3

## Slide 52: Compilation: The Issue
X
B
A
C
D
E
Y
  Attempt 1:
    C - Prefer D over E
    X - Prefer A over B
  Policy:
  (X.A.C.D.Y) >>
  (X.B.C.E.Y)

## Slide 53: Compilation: The Issue
X
B
A
C
D
E
Y
  Attempt 1:
    C - Prefer D over E
    X - Prefer A over B
    Issue:
    Violation of soundness — take a path not specified by the policy
  Policy:
  (X.A.C.D.Y) >>
  (X.B.C.E.Y)

## Slide 54: Compilation: The Issue
X
B
A
C
D
E
Y
  Attempt 1:
    C - Prefer D over E
    X - Prefer A over B
    Issue:
    Violation of soundness — take a path not specified by the policy
    Soundness is easy to handle by filtering bad paths (filter at B)
  Policy:
  (X.A.C.D.Y) >>
  (X.B.C.E.Y)

## Slide 55: Compilation: The Issue
X
B
A
C
D
E
Y
  Attempt 1:
    C - Prefer D over E
    X - Prefer A over B
    B - Filter routes through D
    Issue:
    Violation of completeness — path with preference 2 exists, yet none is taken
  Policy:
  (X.A.C.D.Y) >>
  (X.B.C.E.Y)

## Slide 56: Compilation: An Idealized Example
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:

## Slide 57: Compilation: An Idealized Example
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:

## Slide 58: Compilation: An Idealized Example
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:

## Slide 59: Reversed Automata from Policies
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
Policy:
Reversed automata
tracks BGP message flow
B
A
D
E
C
Z
Y
X
W
  1. (W.A.C.D.out)
  2. (W.B.in+.out)

## Slide 60: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 61: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 62: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)
(D,2,2)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 63: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)
(D,2,2)
(C,3,2)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 64: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)
(D,2,2)
(C,3,2)
(A,4,2)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 65: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(X,1,1)
(D,2,2)
(C,3,2)
(A,4,2)
(W,5, -)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  {1}

## Slide 66: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(Y,1,1)
(X,1,1)
(D,2,2)
(C,3,2)
(A,4,2)
(W,5, -)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  {1}

## Slide 67: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 68: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
Notes: One of the useful properties about the Product Graph…

## Slide 69: Constructing the Product Graph (PG)
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  ACDE
  B
  ACDE
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)

## Slide 70: Constructing the Product Graph (PG)
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
Compact representation of all paths through
the topology subject to policy constraints

## Slide 71: Constructing the Product Graph (PG)
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
0
1
2
3
4
5
  out
  D
  C
  A
  W
0
1
2
3
4
  out
  in
  B
  W
  B
  ACDE

## Slide 72: PG Minimization (Loop analysis)
start
(W,1,1)
(Z,1,1)
(Y,1,1)
(X,1,1)
(A, -,2)
(B, -,2)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(D, -,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
  {2}
  {1}
Must end at W

## Slide 73: Compilation to BGP:
Idea 1: Restrict advertisements to PG edges
  Encode PG state in community tag
  Incoming edges — import filters
  Outgoing edges — export filters
Let BGP find some allowed path dynamically
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}

## Slide 74: Compilation to BGP:
C allows import from D with tag (2,2)
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}

## Slide 75: Compilation to BGP:
C exports to A,B with tag (3,2)
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}

## Slide 76: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
(-,2)
(2,2)
B
A
D
E
C
Z
Y
X
W
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:

## Slide 77: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
(-,2)
(3,2)
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:

## Slide 78: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
(-,3)
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:

## Slide 79: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
(-,4)
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:

## Slide 80: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
B
A
D
E
C
Z
Y
X
W
Not ideal!
A better path exists in the
network, but is not used!

## Slide 81: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Idea 2: Find local preferences
Let BGP find the best allowed path dynamically
  Direct BGP towards best path
  Under all combinations of failures
  Frame in terms of graph algorithms

## Slide 82: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 83: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 84: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 85: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 86: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
choice

## Slide 87: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
  2
  1
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
…
…
choice

## Slide 88: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
  2
  1
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
…
…
Highest preference
obtainable here
choice

## Slide 89: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
  2
  1
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
…
…
But there
could be a
failure!
choice

## Slide 90: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
  2
  1
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
…
…
Sometimes there is
no best choice
choice

## Slide 91: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…

## Slide 92: Compilation to BGP:
start
(Z,1,1)
(Y,1,1)
(X,1,1)
(C, -,2)
(E, -,2)
(D,2,2)
(C,3,2)
(A,4,2)
(B, -,3)
end
(W, -, 4)
(W,5, -)
  {2}
  {1}
Router A
match peer=C comm=(3,2)
export peer←W, comm←(4,2),
comm← noexport, MED←80
Router B
match peer=C
export peer←W, comm←(-,3),
comm←noexport, MED←81
Router C
match[lp=99] peer=E, comm=(-,2)
export peer←B, comm←(-,2)
match[lp=100] peer=D, comm=(2,2)
export peer←A,B, comm←(3,2)
Router D
match regex=(X + Y)
export peer←C, comm←(2,2)
…
Prefer D’s
announce

## Slide 93: Compilation to BGP:
B
A
D
E
C
Z
Y
X
W
The implementation always uses the best available path
B
A
D
E
C
Z
Y
X
W
drop from C
Implementation: C prefers D to E and tags accordingly
  (W.A.C.D.out) >> (W.B.in+.out)
  Policy:
Backup path
Backup path

## Slide 94: Implementation
Benchmarks:
  Network configurations from Microsoft’s networks (Policy from English docs)
  Data center policies (~1400 routers)
  Backbone policies (~200 routers, many peers/router)
  Ignoring prefix, customer group and ownership definitions:
    31 lines for data center
    43 lines for backbone
Propane
Regular
IR
Product
Graph IR
Abstract
BGP
…
Quagga
Topology

## Slide 95: Compilation Time
Data center (< 9 min)
Backbone (< 3 min)
  Parallelize compilation by prefix
  Use artificial topology to explore scalability

## Slide 96: Configuration Size
Data center
Backbone
  Perform configuration minimization during generation
  Avoid using community tags when choices are unambiguous
  Fall-through elimination of route maps